## Slide 1
A Core Robot Algorithm: Inverse Kinematics
Setting a robot’s joints so end effector reaches a target
  Input: current robot geometry
  Output: required joint increments
Computationally intensive problem all limbed robots must solve
Beyond controlling single arms and legs, many larger problems rely on inverse kinematics
  redundant manipulators
  multiple end effectors
  inverse dynamics

## Slide 2
A Digital Accelerator for Inverse Kinematics
Inverse kinematics not well suited for normal digital architectures
  Entirely floating point array, matrix operations
  40% of cycles in inverting matrices
  15% of cycles in sine, cosine operations
We solve IK via damped least squares
  Dedicated sine, cosine function generators
  Parallel, fixed-point functional units
  Solves IK problem in 100μs: compare against 10ms for general algorithm on CPU

## Slide 3
Architecture and Timing Design
Architectural Choices
  Pipelining sine/cosine and array multiply
  Parallelized matrix multiply and matrix inversion
  Fixed point representations throughout system
Timing Choices
  Single array of multipliers shared amongst modules
  Aggregate individual enable and done signals into global state machine

## Slide 4: Experiences and Issues
Deciding on the algorithm to use
Determining what implementation would fit on
the board
Convincing ourselves the algorithm works
Extensively tested the core hardware, but not the
top-level interface (until yesterday)

## Slide 5
Lessons Learned
Test the whole stack earlier
Plan before trying to implement
Use timing diagrams and area estimates before touching hardware
Leave no ambiguity in the design