## Slide 1
Outline
an overview of the project and its objectives,
a discussion of the architectural and timing design
  New hardware architecture diagram
experiences and issues in implementation (the difficult parts)
  Fixed point accuracy and precision
  FPGA resources
  Driver data movement
a summary including lessons learned

## Slide 2
A Core Robot Algorithm: Inverse Kinematics
How to control a robot’s joints to achieve desired pose
  Input: current robot geometry
  Output: required joint increments
Computationally intensive problem all limbed robots must solve
Beyond controlling single arms and legs, many larger problems rely on inverse kinematics
  redundant manipulators
  multiple end effectors
  inverse dynamics

## Slide 3
A Digital Accelerator for Inverse Kinematics
Inverse kinematics not well suited for normal digital architectures
  Entirely floating point array, matrix operations
  40% of cycles in inverting matrices
  15% of cycles in sine, cosine operations
We’ve created an accelerator to solve IK via damped least squares
  Dedicated sine, cosine function generators
  Parallel, fixed-point functional units
  Solves IK problem in 4μs: compare against 10ms for general algorithm on CPU

## Slide 4
Fixed Point
Varying number of bits
  Always 16 bits for fraction part
    1/2^16 smallest increment between numbers
  Average 16 signed bits for integer part
Fixed point numbers use integer arithmetic
  Smaller design than floating point megafunctions
Loss of precision during certain operations
  Multiplications result in a number twice as large as original numbers being multiplied. Need to truncate
  Division results in number half as large unless shifted before which can save precision
  Square root results in number half as large and cannot be fixed by shifting
Software converts from floating point to fixed point so FGPA only sees fixed point

## Slide 5
Lianne's Lessons Learned
Plan before trying to implement
Need to use timing diagram to understand which steps have to happen in what order to maximize resource sharing and parallelism