## Slide 1: A Core Robot Algorithm: Inverse Kinematics
How to control a robot’s joints to achieve desired pose
  Input: current robot geometry
  Output: required joint increments
Computationally intensive problem all limbed robots must solve
Beyond controlling single arms and legs, many larger problems rely on inverse kinematics
  redundant manipulators
  multiple end effectors
  inverse dynamics

## Slide 2: A Digital Accelerator for Inverse Kinematics
Inverse kinematics not well suited for normal digital architectures
  Entirely floating point array, matrix operations
  40% of cycles in inverting matrices
  15% of cycles in sine, cosine operations
We’ve created an accelerator to solve IK via damped least squares
  Dedicated sine, cosine function generators
  Parallel, fixed-point functional units
  Solves IK problem in 4μs: compare against 10ms for general algorithm on CPU